## Slide 1: IEEE International Workshop on Computer Aided Modeling and Design of Communication Links and Networks
OpenCV2X Mode 4: A Simulation Extension for Cellular Vehicular Communication Networks
http://www.cs.ucc.ie/cv2x/
Brian McCarthy and Aisling O’Driscoll
b.mccarthy@cs.ucc.ie and a.odriscoll@cs.ucc.ie
This publication has emanated from research conducted with the financial support of Science Foundation Ireland (SFI) under Grant No: 17/RC-PhD/3479.
Notes: louder on voice

## Slide 2
Vehicular Ad-Hoc Networks (VANETS)
  Originating from MANETS (Mobile Ad-Hoc Networks).
  Application of Computer networking techniques to vehicles.
Vehicular Networking 1/4
Enables inter vehicle communication for services;
  Safety Services, vehicle notification about collisions
  Cooperative traffic efficiency.
  Infotainment. (video streaming)
[1] Arena, F.; Pau, G. An Overview of Vehicular Communications. Future Internet 2019, 11, 27.
Notes: ITS ->
Too many acronyms.
Important to highlight how do we know it works.

## Slide 3
802.11p Wi-Fi variant (DSRC/WAVE) V2X IT-G5.
  OFDM (Orthogonal Frequency Division Multiplexing).
  CSMA/CA (Channel Sensing Multiple Access with Collision Avoidance).
  Issues around Congestion Control in Dense environments.
  Well investigated in academia, trials, commercial equipment and deployments.
C-V2X (Cellular Vehicle to Everything) (LTE-V) Cellular equivalent.
  Recently defined by 3GPP release 14.
  Release 15 - 5G new radio.
  SC-FDMA (Single Carrier – Frequency Division Multiple Access).
  SB-SPS (Sensing Based Semi-Persistent Scheduling).
  Ready-made infrastructure.
  As yet limited investigation.
Vehicular Networking 2/4
Notes: ITS ->
Too many acronyms.
Important to highlight how do we know it works.

## Slide 4
Current regulator vacuums in the US and EU has led to delay in 802.11p deployments.
Vehicular Networking 3/4
CV2X Backers
DSRC/WAVE Backers

## Slide 5
Applications and standards:
  Cooperative Awareness and ITS applications.
  ITS-G5 and WAVE - 802.11p based standards.
Goal:
  Enable the vehicular networking community in its investigation of CV2X standard.
  Incorporate current day standard application and upper layers with a compliant 3GPP CV2X implementation.
Vehicular Networking 4/4
Notes: ITS ->
Too many acronyms.
Important to highlight how do we know it works.

## Slide 6
Existing C-V2X (Rel 14) simulation models.
  Are not publicly available [1].
  Concentrate on link layer simulation [2,3].
  Do not offer integration with existing Vehicular networking standards such as ITS-G5.
  Available across numerous different simulators such as MATLAB. Ns3, OMNeT++.
  Capture the system level simulation aspect.
  Open Source full stack implementation.
Current Solutions
[2] R. Molina-Masegosa and J. Gozalvez, “System level evaluation of lte-v2v mode 4 communications and its distributed scheduling,” IEEE 85th Vehicular Technology Conference (VTC Spring), pp. 1–5, June 2017.
[3] G. Cecchini, A. Bazzi, B. M. Masini, and A. Zanella, “Ltev2vsim: An lte-v2v simulator for the investigation of resource allocation for cooperative awareness,” in 2017 5th IEEE International Conference on Models and Technologies for Intelligent Transportation Systems (MT-ITS), June 2017, pp. 80-85.
[4] D. Wang, R. R. Sattiraju, A. Weinand, and H. D. Schotten, “System-level simulator of LTE sidelink C-V2X communication for 5g,” CoRR, vol. abs/1904.07962, Apr 2019. [Online]. Available: http://arxiv.org/abs/1904.07962
Notes: - Open Science.
- No concentration on the App layers.
- Not compliant with standards.
- Multiple different platforms makes direct comparison more difficult.
33s

## Slide 7
Mode 3:
  Scheduled
  eNodeB Schedules resources for UEs
Mode 4:
  Autonomous
  UEs select their own resources
  Sensing Based Semi-Persistent Scheduling (SB-SPS)
Cellular Vehicle To Everything

## Slide 8
Channel broken into subchannels and subframes.
Channel split into PSCCH for sidelink control information (SCI) messages and PSSCH for transport blocks (TBs).
SCI messages act as control for channel.
Channelization

## Slide 9
MAC layer maintains scheduling grant for a certain period, sending at regular intervals in that period. E.g. 100ms
PHY layer selects Candidate Single-Subframe Resources (CSRs).
CSRs are selected based on sensing information (previous SCIs, channel quality measurements).
Selection and Sensing

## Slide 10
On transmission the MAC layer informs the PHY layer to send an SCI message.
Resource insufficient to support the TB then the reservation is broken and a new reservation is made.
SCI sent in all cases with or without TB.
Transmission

## Slide 11
Prevalent Vehicular simulator is OMNeT++
  Veins for system level simulation.
Artery [4]:
  OMNeT++ for network traffic simulation
  Uses SUMO for road traffic simulation
  Artery integrates the ITS-G5 standard for the upper layers.
SimuLTE [5]:
  Provides an implementation for LTE in OMNeT++
Our bespoke C-V2X Mode 4 implementation builds upon these for Mode 4 simulation.
Implementation
[5] R. Riebl, H. Gunther, C. Facchi, and L. C. Wolf, “Artery: Extending veins for VANET applications,” in 2015 International Conference on Models and Technologies for Intelligent Transportation Systems (MT-ITS), Budapest, Hungary, June 3-5, 2015, 2015, pp. 450–456. [Online]. Available: https://doi.org/10.1109/MTITS.2015.7223293
[6] A. Virdis, G. Stea, and G. Nardini, “Simulating lte/lte-advanced networks with simulte,” in Simulation and Modeling Methodologies, Technologies and Applications, M. S. Obaidat, T. ̈Oren, J. Kacprzyk,and J. Filipe, Eds. Cham: Springer International Publishing, Jan 2016, pp. 83–105.
[7] Study on LTE-based V2X services (v14.0.0, Release 14), 3GPP, July 2016, 3GPP TR 36.885.
Notes: Highlight the bespoke implementation.
The integration of

## Slide 12
Implementation: Overview of architecture
Notes: Artery SUMO and apps, message layers
Vanetza ITS-G5 implementation.
Red is new layers of the stack.
Grey is adapted for Non-IP traffic.
SimuLTE IPV4 Artery IPV6
Pinky red.
Change the bottom one to white and it’s more obvious, change up the colours. Make it more obvious

## Slide 13
Implementation: Message Sequence Diagram.
Notes: Explain Scheduling with this.
CSR selection.
1:37
Animating + lazer pointer
Relate to what impact it makes on the performance.
Relate to real life.

## Slide 14
Scenario Description
Highway Fast:
  200 vehicles at most dense at 140 km/h
Highway Slow:
  380 vehicles at most dense at 70 km/h
[8] Study on LTE-based V2X services (v14.0.0, Release 14), 3GPP, July 2016, 3GPP TR 36.885.
Network Configuration | 
Winner+ B1 LOS | 16 RBs per subchannel
Nakagami Fading | MCS 5 & 7
10 MHz Bandwidth (48 RBs) | Tx Rate 10 Hz
23 dBm transmission Power | 190 Byte + 300 Byte packets
3 Subchannels | 
SB-SPS parameters:
  ProbResourceKeep
  Sensing Window Length
Packet loss causes
2 Vehicular Scenarios
Statistic:
  Packet Delivery Rate
Notes: 1:13s
Put it all in the table. Mobility pattern, highway fast + slow and describe.
Highlight vehicle count, BOLD
Better explanation of the scenarios.
What does that mean when PDR less than 80%.
Contribution, the results examples of what you can do with it.
What do people know about CV2X
LTE vs 802.11p
Number of simulations for each and get them all at the same level.
Highlight that this is from the standard

## Slide 15
Results 1/4
ProbResourceKeep
  Controls the likelihood of maintaining a grant once allocated.
  Higher probability means greater likelihood of losing grant
Notes: 1:24s
Break into two slides to show it more easily. Increased size.
Colours are the same for the best results.
Say Fast.
Look at slow for ProbResourceKeep more interesting.
What's the ratio of the received from one individual. Might be more interesting.
Spoof attacks and their impact.

## Slide 16
Results 2/4
Sensing Window Length (swl)
  History of SCIs and RSRP/RSSI measurements maintained.
Notes: 1:24s
Break into two slides to show it more easily. Increased size.
Colours are the same for the best results.
Quality

## Slide 17
Results 3/4
Packet loss causes
  Initially primary cause is Interference from others
  As distance increases propagation loss become the primary factor in packet loss
Notes: 47s
2 Slides.
Make a point on the point when propogation goes past interference

## Slide 18
Results 4/4
Comparison of Fast and Slow
  As shown congestion has a significant impact on performance of CV2X
Notes: 47s
2 Slides.
Make a point on the point when propogation goes past interference
Quality

## Slide 19
Thorough analysis of CV2X simulation parameters.
  RSRP thresholds.
  RSSI threshold for CBR.
CV2X Mode 4 performance for Non-periodic traffic.
  Current periodic beaconing.
  Constant breaking of reservations leading to inefficient use of resources.
Congestion control mechanisms
  Decentralised Congestion Control (DCC).
  3GPP specified mechanisms.
  Absence of work, as it's SB-SPS is a competitive access mechanism.
Future Work
Notes: Non-Periodic:
SB-SPS "Semi-Persistent" bad if not persistent
Congestion Control:
Obviously not going to fix all issues, mechanisms will need to be looked at.
Mode 3:
Good for ITS applications such as traffic management, any distance comm between vehicles.
1:40

## Slide 20
A freely available, open-source implementation of the 3GPP Release 14 C-V2X Mode 4 standard.
With the inclusion of the current ITS-G5 will enable a more robust investigation of the CV2X standard.
Our Contribution

## Slide 21
Please feel free to contact me:
Brian McCarthy – University College Cork
b.mccarthy@cs.ucc.ie
The model is available here
http://www.cs.ucc.ie/cv2x/
&
GitHub
https://github.com/brianmc95/OpenCV2X
Thank you for your time.
Notes: Software release date.
Generic
Put email there instead.